## Slide 1: Best Practise Guidance
Test Accuracy & Charging Scenarios

## Slide 2: Introduction
The T&D forum were asked to provide some guidance on Openreach test accuracy, when there may be scenarios which drive charges, and what could be done to avoid those scenarios.
The following slides offer some advice gleaned from discussion between CPs and Openreach in this area.
It is intended to be a “living” document which can be updated as required with new information.
Initially we have attempted to answer the following questions:
How accurate is Openreach line testing?
Why are the results not black and white?
What can CPs do to minimise the jobs which may result in a charge?

## Slide 3: No line testing can be 100% accurate
Every line in the country has a unique set of circumstances, so there is no generic set of standards that can pinpoint what will affect each specific line’s electrical signature to cause a service impact.
Test systems are set up initially to identify those well defined circumstances that would definitely impact the majority of lines with certain faults, such as complete breaks (DIS).
More work then is needed to identify more and more granular signatures and changes, which impact smaller and smaller pots of lines.
CPs and Openreach agree that a system cannot be 100% accurate when such diversity of circumstances exist. However we can highlight some of the known “blind spots” of line testing and by understanding these weak spots we can learn how they might be mitigated.
An important point to remember here is that the TAM test is looking at the electrical parameters of the line tested. Changes to these parameters can impact the broadband service, but there are also many other issues that also degrade the data quality and it’s important to ensure that all the data available is looked at where there is a broadband fault.

## Slide 4: Some known “Blind Spots”
Test system limitations – there are limitations in the actual technology of the systems used for testing, e.g. single ended tests are less accurate than hand held tests, which are a method of double ended testing, especially on longer lines. Openreach use hand held testers when visiting the network (i.e. on a live fault) which can provide more accurate results. It should be noted that TAM tests are single ended tests. The TAM system could develop a fault which may then result in an erroneous test result, therefore making the root cause less clear.
Complex home environments – test systems work by identifying an electrical signature. The number of devices in the home is growing & some have begun to show electrical signatures similar to network faults when they break. By asking users to remove all CPE from the line before re-running tests CPs can identify if this is the case before logging a fault to OR.
Test system requirements – some tests may require specific setup to work effectively. CIDT tests are much more accurate in identifying HR situations, but they need to be run while the modem or router is attached to the line and on.
Non electrical faults – some fault types do not trigger a test fail because they are not impacted by an issue that shows a change in the electrical signature. These faults, such as crossed lines, can only be identified with further diagnostic questioning.
Data input – if the data set that the system is using to make it’s calculations is not correct, such as the line length, then the results coming out may not be accurate.

## Slide 5: Test Reporting Accuracy
Currently where testing identifies an issue (LTNOK) it appears to be more accurate (c90% of jobs are cleared in the OR domain) than where no problem is found (40% of LTOK jobs are cleared in the OR domain). Improving LTNOK accuracy is important to prevent inaccurate charges to CPs, while better LTOK accuracy is required to increase CP confidence in the OR testing. In turn this could help drive down repeat faults and reduce truck roll.
Openreach are working with CPs to identify those elements of both LTOK and LTNOK which are biasing the results. For example:
LTOK tests which do not get faults reported are not currently included in the LTOK accuracy figure
LTNOK circuits where an incident is either fixed outside of the fault report, or clears itself may generate FNF clears
Openreach are also looking to include an element of effectiveness in their reporting to help give CPs confidence in their results. This means that post job line data and clear information will be looked at to determine if a fix matched the test result. Openreach hope this will help reduce the ineffective comfort clears whilst allowing proactive network uplifts to be identified as effective resolutions.

## Slide 6: How does this work in the real world?
Where a fault is given an FU/LN/CE MFL and an engineer cannot find a fault in the network or the home domain, the issue must be cleared as Fault Not Found and cannot be charged to the CP.
This changes if the engineer gains access to the home and a fault is identified in the CP/EU domain. The job can then incur a TRC clear & charge for the work to identify the fault.
CPs can choose to use the TRC flag to prevent OR from fixing the identified issue, leaving them to discuss options for completing this chargeable work with their End customers.
Openreach looked in detail at the LN and CE MFL for copper faults and identified some learnings…
On average the CE T-codes prompt a 20% access request rate
20% of CE MFL test results may generate a CP charge from a CP/EU fix or a RWT clear
Of those that get access 20% of jobs will not have a fault identified
Even though some of these could be dynamic issues this will drive a RWT charge
On average the LN T-codes prompt a 5% access request rate
This pot includes things like faulty CPE in the home mimicking a network issue.
There are no specific LN or CE T-codes that would be better always appointed
Some codes do have more home clears, but no pot would be better always appointed.

## Slide 7: LTNOK journies and their clear codes
LTNOK Scenario | EC Premises Visit | Clear Code | CP Charge
Engineer clears network No faults identified | No | 51.2 - Fault Not Found | No
Engineer clears network Issue suspected within EC premises EC agrees entry No faults identified | Yes | 51.2 – Fault Not Found | No
Engineer clears network Issue suspected within EC premises EC refuses access/not available | No | 51.2 – Fault Not Found Or Job furthered back for an appointment | No
Engineer clears network Issue suspected within EC premises EC agrees entry EC caused damage Internal or External | Yes | 60.6 – BT Network – NTE/block terminal or LJU | Yes
Engineer clears network Issue suspected within EC premises EC agrees entry EU Wiring | Yes | 16.2 – Non-Openreach Maintained Equipment | Yes
Engineer clears network Issue suspected within EC premises EC agrees entry Faulty NTE | Yes | 60.5 - Fault found on BT maintained equipment at the customer premises | No

## Slide 8: Context is key
It’s clear that while the electrical test system is very useful, CPs need to use all the tools at their disposal to ensure the best and most effective outcome for their customer.
Aligning the test data with contextual information and the customer experience often helps guide to the right conclusion…
What is the EU telling you? Identify your problem statement
What is your data telling you? Collect your broadband data and any other information you have
What does the line test tell you? Use the TAM or Service test to help guide your diagnostics steps
Always be aware that there may be more complex scenarios in play, such as multiple faults on a line, or dynamic problems.
Issues caused by interference or line degradation can sometimes not show on test results or show a faulty signature which then disappears.
These types of issues can create uncertainty and make it difficult to be sure what the right action should be. At these times going back to the customer and getting them to help identify any pattern of behaviour can be invaluable. If you have an idea when something is going to happen, it may make it easier to capture that faulty test result.

## Slide 9: Not all faults can be fixed
It must be understood by CPs that not all faults can be fixed, even where test data does point at an issue. Some of these scenarios have been shared below.
3rd party REIN issues
Long copper lengths
Cross talk
Some issues, whilst not impossible to fix, can cause delays or complexity which means they may not be completed. This might be a capacity issue limited by planning challenges, or a fault which needs awkward dig work.
The end customer is also a factor here, they may choose not to have the issue remedied as the fix will cause them disruption. For example where a customer chooses not to stop using a faulty extension, or won’t replace wiring behind radiators.
When these scenarios are suspected, often Openreach can help identify the issue by working with the CP, but often they cannot enforce a fix and so CPs should be prepared to manage those situations with their customers.