## Slide 1: Best practice guide - Raise and Manage a Customer Fault
28 September 2016
Version 1.1

## Slide 2: Introduction
This best practice guide provides key information that will assist you when raising and managing fault reports and enable Openreach to effectively resolve your customers issue.
When followed, this guide will help reduce the likelihood of customer no access or readiness issues and will better equip our engineers to restore your customer’s service quicker.
The guide covers the repair customer journeys across our product portfolios - Wholesale Line Rental (WLR), Local Loop Unbundling (LLU-SMPF/MPF) and Generic Ethernet Access (GEA-FTTC).
Step-by-step, the guide will take you through the key information that you should capture as a Communications Provider (CP) at the point of distress to submit to Openreach within a fault report including;
  Capturing and supplying information relevant to the End Customer and Home/Premises Environment
  Capturing and supplying information relevant to the Service consumed by your customer
  Capturing and supplying information relevant to you, the CP
  Effective inflight fault management and communication
Please Note: There is also a section for your development and IT teams to ensure information, that is captured by your agents, is transmitted to us in the relevant fields. An annex has been provided to cover elements that should be referenced throughout the fault management lifecycle, i.e. how to access information on Major Cable Breakdowns/Service Outages etc.
Raise and Manage a Customer Fault
2

## Slide 3: Point of Distress
The following guide takes you through the detail that we require to enable a successful resolution of your customer issue. The information contained within this guide is equally relevant to our engineers undertaking additional problem resolution services that can be ordered such as Special Fault Investigation (these can be product specific offerings).
If your customer has contacted you to report a potential fault with their service, ensure that you have carried out all the appropriate diagnostic tests prior to submitting a fault into Openreach.
Please ensure that you have taken the time to walk your customer through each of the relevant set of structured questions for the service they are consuming prior to raising a fault with Openreach. For example, you may be able to avoid an engineering visit and saving your customer time and inconvenience, by ensuring your customer has unplugged their equipment at the NTE when running a standard line test and is not speaking on the impacted line whilst you complete an Openreach line test.
If you are unable to resolve the issue with your customer remotely and you require Openreach to undertake further diagnostics, please raise the appropriate fault type into Openreach and ensure that a full description of the fault is provided within the relevant notes fields. Please ensure you ask the customer to think through how to access all of their current services, including extensions. If they have extensions in difficult to reach places (e.g. upstairs/lofts/external to main premises) make sure that access is available. You should notify us beforehand if there are any health and safety issues or access challenges of which our engineers need to be aware of.
Please Note: If your customer is in a rented property, there is likely to be an obligation that they make their landlord aware of any new installation work and to obtain full permission in advance. In some cases landlords may restrict certain types of work, e.g. drilling or the location of equipment, which can also apply to a repair. In such instances you will need to ensure that you follow your own local policies regarding advice to your customers on their obligations to any landlord.
Raise and Manage a Customer Fault
3

## Slide 4: Point of Distress
End Customer and Home/Premises Environment Information
Subject | Best Practice
Provide Primary and Secondary Contact Information | Please ensure the contact information provided is that of a mobile or alternative working line. The engineer will always attempt to ring your customer prior to arrival and will use these contacts if they are unable to locate or gain access to the premises. On non-appointed faults, the engineer may attempt to contact your customer to gain additional information regarding the problem they are experiencing as this insight will assist with fault resolution. Named contacts, secondary telephone numbers and alternative contacts all help to ensure that any remedial action goes ahead as planned to resolve your customer issue. When our engineer contacts your customer, the number presented to them will vary depending on the line used to make a call, so customers should accept any call including ‘0800’, ‘withheld’ or ‘unavailable’. You can provide this information within four elements: Primary Contact - The ‘ContactName’ [50 Characters], the ‘Telephone’ [11 Characters], ‘SecondaryTelephone’ [11 Characters] and ‘email’ [100 Characters]. You can also provide contact details for an alternative contact and supply this within the ‘ContactName’ [50 Characters] and ‘Telephone’ [11 Characters] fields. Openreach engineers cannot enter premises unescorted or where the only person in attendance is a minor. Please ensure that any named contact is made aware of the work being undertaken and is available on the numbers supplied for the duration of the appointment (especially if this is a representative of your actual customer) and that the person is authorised to advise our engineer, make decisions and give the engineer access to the property. If the premises are multi-occupancy, e.g. business units or flats your customer will need to ensure access is available to the telephone distribution point or communications room. They may need to arrange this with their landlord or other relevant authorised person. (See - APPENDIX B)
4

## Slide 5: Point of Distress
End Customer and Home/Premises Environment Information
Subject | Best Practice
Provide Company Name Details | When placing a fault for a customer at business address, you should add the business name to the ‘CompanyName’ [100 Characters] field within the fault. This should be “the name above the shop door” i.e. the information that should be visible to the engineer, e.g. Although the customer contracting the telephone service maybe “Dixons Stores Group”, it is better to supply the name for the given location as “PC World Currys“ as this would be the name above the shop door.
Provide all Relevant Site Specific Health and Safety Related Information | Health & Safety related information should be supplied on all faults within the ‘HSHazards’ [100 Characters] notes field, e.g. If the customer premises contains a Flat Roof, we will need to send specifically skilled engineer to attend, so please state Flat Roof. Examples of Hazards that you could capture are:- Asbestos Hazard, Dangerous Animals, Dog On-site, Flat Roof, Fragile Roof, High Voltage Overhead power lines in vicinity of work area, *Hot Site, Railway Working, Working at Height restrictions apply. *Hot Sites = All power generation/distribution facility and/or Area surrounding power generation/distribution facility This should clearly state if any health and safety issues are associated with the site or customer premises, if there are none, then the word ‘NONE’ should be written. Please Note: Please also include the RAMS reference number within this field, if any Risk Assessments of Method Statements have been provided to the end customer. e.g. ‘RAMS 12 Internal Cabling supplied to customer’ or ‘RAMS 1 Customer Wiring’ etc. (See - APPENDIX A) Warning: The Hazard field should not be used to provide personal and/or sensitive information regarding the end customer
5

## Slide 6: Point of Distress
End Customer and Home/Premises Environment Information
Subject | Best Practice
Booking appointments | Openreach offers a range of appointments, covering different time periods throughout the working day. Please ensure that your customer is aware that our engineer could arrive anytime within the appointment slot and the engineer may work beyond the appointment slot to restore service and an authorised representative will need to be present throughout. Once you have selected the appropriate appointment for your customer, please provide this reference within the ‘AppointmentReference’ [8 Characters] field.
Provide Access Details Information | Openreach provide a number of fields where you can signpost access restrictions that could impact Openreach resolving your customer issue. You can provide full access details within the ‘AccessDetails/Notes’ [255 characters] field detailing any site related information. For example: where our engineer is required to have special security/clearance, where parking restrictions exist or any other special considerations such as “knock loudly bell broken…” should also be noted. When applicable provide an ‘EarliestNextAccessDateTime’ [DD/MM/YYYY HH:MM:SS] to signpost when your customer will be available from. You can provide a ‘LatestAccessDateTime’ [DD/MM/YYYY HH:MM:SS] to signpost when your customer will be available until, this is only referenced when placing un-appointed trouble tickets. If 24 Hour Access is available, you can select ‘TwentyFourHourAccess’ ‘Y’ and this can be used in certain circumstances as an alternative to an appointment, but this only applies when Service Maintenance Level 3,4,30,40 are associated to the service. Please Note: Requesting time restrictions within the appointment slot selected could result in charges being raised, if access cannot be gained by the engineer at any time during the appointment slot.
6

## Slide 7: Point of Distress
Service Related Information
Subject | Best Practice
Provide the Service ID | The Service identifier is a mandatory field that needs to be provided within the ‘ServiceID’ [11/12 Characters] field. This can only be supplied by the owning CP of the asset and identifies the service as Openreach provided. For example: WLR=02080000000, SMPF/MPF=LLXX0000000, FTTC=OGEA00000000.
Provide the Telephone Number of the Service (If Voice Provided) | If you are providing a voice service (non-WLR), please provide the Directory Number (DN) within the ‘VoiceServiceDN’ [11 Characters] field. This is the number associated to the service your customer will recognise. As fall back you can provide a structured message within the ‘Notes’ [255 Characters] field ‘DIAL TONE PRESENT - DN:xxxxxxxx’ as we can perform additional tests to confirm that the line is working. This test requires dial tone, routing of an 0800 number and presentation of the calling line identifier to our test system call platform. However, if the circuit has been provided for data only and does not have dial tone for example: LLU MPF, please make this clear in the ‘Notes’ [255 Characters] field as engineers will test for dial tone. Please enter the following note ‘DATA ONLY MPF – NO DIAL TONE’
Supplying the Service Maintenance Level (SML) | The Service Maintance Level should be provided within the ‘ServiceLevel’ [4 Characters] field and typically should reflect the service maintenance level on the asset unless you are attempting to purchase additional services within the fault report or expedite the fault report. When attempting to order additional services within the trouble report: i.e Harmonised Repair you need to indicate this within the ‘OrderRevisedServiceLevel’ [1 Character] field with a ‘Y’.
7

## Slide 8: Point of Distress
Service Related Information
Subject | Best Practice
Providing a Short Description of the customers issue in their words | Providing a short description of the issue, in the customers own words, needs to be provided in the ‘Short Description’ [80 Characters] field. This empowers the engineer to have an informed discussion with the customer as part of the ring ahead process, giving confidence that the engineer understands the customer’s issue and why they have been contacted to work on the customer’s service. Examples are ‘the phone in the master bedroom no longer works’ or ‘unable to download xxx and my device is telling me its due to a broadband issue’ or ‘our front desk team are not receiving inbound calls and broadband is down’
Providing a Long Description of the Customers problem | Providing a long description of the issue, that is enriched with your service related information and the cumulative diagnostic information will enable our engineer to more effectively resolve the customers issue, this should be provided within the ‘Long Description’ [5000 Characters] field. Any additional information you have captured concerning the customer issue and the history of the customers service, including any previous Non Openreach engineering visits obtained through structured questioning or through your own knowledge/diagnostics/service layer information, can also be provided in this field. Further details of the type of information we would expect to see within this field (See - APPENDIX C)
Providing a Fault Code | Once you have identified the appropriate fault category for the issue experienced by your customer, you can provide this 3 letter code within the Fault Code [4 Characters] field. (See - APPENDIX D). It is important to ensure that you have correctly categorised the fault as a number of these codes will drive a specific process to ensure you customer’s fault is resolved effectively, by the most appropriate resources within Openreach. Please Note: Damage Reports, specifically DRO (Damage Report Overhead) and DRU (Damage Report Underground) are explicitly used to indicate an incident that has resulted in damage to the Openreach network. We treat these reports very seriously and recognise that they may indicate a Health and Safety issue that requires our urgent attention and response.
8

## Slide 9: Point of Distress
Service Related Information
Subject | Best Practice
Providing Test Information | Once you have completed your structured questions and own tests, it is important to run the appropriate tests with Openreach to establish the most effective channel to manage your customers issue. Once you have decided that you wish Openreach to progress with the issue resolution, you should provide the reference number of the test you have conducted within the ‘TestReference’ [64 Characters] field. If the fault is of a nature that would not require a test to be run, e.g. External ‘Damage’ you can provide the appropriate value within the ‘NoTestReason’ [80 Characters] field. This is also applicable when you experience issues running the appropriate Openreach tests. If the line test comes back as the line is testing OK, we have a range of test products that you can select to drive a specific customer experience journey (process) to resolve your customer’s issue, once you have selected the appropriate test product you can provide this within the ‘TestProduct’ [80 Characters] field.
Providing a Test Account User Name and Password | When raising a fault into Openreach to resolve an issue with your broadband services, you can provide the test account, test user name, test password, IP and URL details to our engineers that will enable them to test the service you are providing to your customer, these can be provided within the ‘TestAccountDetails’ {255 Characters] field.
Providing your Agreement to Additional Charges | There are a range of fields that enable you to manage your customer experience and potential associated costs. You can indicate the upper level of time related charge banding within the ‘UpperTRCBand’ [1 Character] with a range value from 0-4, pre-authorising the engineering time to complete additional work to restore your customers services, this can be provided within. You can then pre-authorise additional charges for premium services and notify this within the ‘AcceptAdditionalCharges’ [1 Character] field with a ‘Y’. When you chose one of these premium services, i.e. expedite or chargeable appointment, you will need to indicate that you agree to the terms and conditions and additional charges by completing the ‘AcceptTermsAndConditionsCharges’ [1 Character] field with a ‘Y’.
9

## Slide 10: Point of Distress
CP Contact Related Information
Subject | Best Practice
Providing Co-Op details to aid fault resolution | In some circumstances an engineer may need to co-op with the CPs technical department to isolate issues or restore service, this is only included within a sub-set of our repair portfolio offerings. If this is a service that you require, you can notify us that you are able to support inbound co-op calls by providing a ‘Y’ within the ‘Co-OpCallRequested’ [1 character] field. If you have provided your Co-Op call preference, you can now provide the number of technical department or CP engineer, within the ‘DetailedContact/Telephone’ [11 characters] field. You can also provide additional information within the Co-Op notes field, this includes any extension numbers to route the call to the appropriate team/individual or additional details regarding arrangements for onsite co-op, please provide these within the ‘Question/QuestionValue’ [5000 characters] field. Some of our repair portfolio variants also support the ability to request a joint co-op meeting at either the exchange or the customer location, you signpost this within the ‘Co-OpLocation’ [100 characters] field with either ‘CA’, ‘FU’ values. You will also need to provide a date and time for this meeting and this should be provided within the ‘Co-OpDateTime’ [19 characters] field, the format for providing this is [DD/MM/YYYY HH:MM:SS] When selecting any of the above options, we will need to know who we are going to contact, you should provide either the name of technical department or the name of your engineer who will be attending the joint meeting, within the ‘DetailedContact/ContactName’ [50 characters] field.
10

## Slide 11: Point of Distress
CP Contact Related Information
Subject | Best Practice
Providing CP Contact Details | As the CP you can provide a range of information to Openreach dependent on how you would like to be contacted throughout the repair process if our desk or field based engineers require your assistance to resolve your customer’s issue. Supplying the reference number that you have provided to your customer when accepting the issue enables Openreach desk and field engineers to have an informed ring ahead or door step conversation, giving your customer the confidence that our engineer is working on behalf of you, the CP. This can be provided in the ‘RefNum’ [64 Characters] field. You can provide the first and last name of a dedicated individual managing you customer issue or a name that represents the team the call will be routed through to within the ‘DetailedContact/FirstName’ and ‘DetailedContact/ContactName’ [50 characters] fields. This should either the individual or team that are accountable for management of resolution of the customers issue within your business. The number to contact this individual/team on can be provided within the DetailedContact/Telephone [11 characters] field and the email address can be provided within the ‘DetailedContact/Email’ [100 characters] field.
11

## Slide 12: Managing In-flight faults
Appointments
Subject | Best Practice
Managing appointments on in-flight faults | You should contact your customer prior to any Openreach appointment to ensure your customer is aware that an engineer will be attending their premises. If your customer notifies you that they will not be available at this time, please amend the fault to include a new appointment that has been agreed with your customer. For WLR, if Openreach misses an appointment we will attempt to contact your customer to rearrange and you will be notified by a KCI if we are successful. If we are unable to rearrange the appointment, we will make an automated appointment for 48 hours in the future and notify you with a KCI requesting that you contact your customer to confirm the rearranged appointment. For WLR if the appointment is missed due to your customer, Openreach will send a delay KCI requesting that you rebook. You have 72 hours to amend the fault prior to it being cancelled and you will receive a reminder after the first 48 hours. For LLU and SFFA/NGA, if Openreach misses an appointment we will attempt to contact your customer to rearrange and you will be notified of the new appointment time if we are successful. If we are unsuccessful we will send you a KCI to advise that you will need to re-book. For LLU and SFFA/NGA, If the appointment is missed due to your customer, Openreach will send a delay KCI requesting that you rebook. You have 72 hours to amend the fault prior to it being cancelled and you will receive a reminder after the first 48 hours.
12

## Slide 13: Managing In-flight faults
Fault Tracker
Subject | Best Practice
Fault Tracker | The Fault Tracker is a self-service tool that enables you to proactively review the Field/Desk Engineering Notes relating to the faults you have raised with Openreach and will reduce the need to contact the Openreach SMC. http://www.openreach.co.uk/orpg/home/products/serviceproducts/orderandfaulttracker/orderandfaulttracker.do Online support material is available via the link below to maximise the benefit you receive from this tool http://www.openreach.co.uk/orpg/customerzone/products/serviceproducts/orderandfaulttracker/businessprocess/orderandfaulttrackerprocessdescription.do
13

## Slide 14: Managing In-flight faults
Cancellations
14
Subject | Best Practice
Managing fault cancellations | If you are notified by your customer that the fault should be cancelled you should notify Openreach immediately. The Point of No Return (PoNR) on a fault is when an engineer is despatched and this is signalled by sending a KCI with response code 3200 ‘Engineer Dispatched’. If the fault is prior to the PoNR, please cancel the fault via the system. If the fault is beyond the PoNR, you will need to contact the Openreach Service Management Centre immediately to try and avoid an engineer being sent out. If an engineer has been tasked you could be charged an abortive visit charge. Openreach will accept a cancellation of a fault (inc SFI) up to the PoNR, standard cancellation charges will not apply, but you may still be subject to other charges based on the combination of fault report and appointment you have selected.

## Slide 15: Best Practice for the CP IT Design Community
As our CP customer IT design community, you have the ability to ensure the solutions work effectively and efficiently end to end. You share responsibility for increasing the success of these solutions from the first customer contact, to your customers issue being resolved.
If you ensure the right information is captured, in the correct format and character length and passed to Openreach in the relevant fields, this will enable Openreach to present the correct information to the relevant parts of our desk based and field workforce. Specialist access information is an example of key information that if we’re aware of upfront, will enable our engineers to gain access effectively first time.
The following slides highlight key information that your can guide your agents to capture and record in the correct fields to pass them onto Openreach. It is very important to note that each of these fields have character length limits and any extra characters you may provide will get truncated and important information may not reach us. Hence it is key that you highlight to your agents, where possible, if they have exceeded the information for a specific field.
If you are a B2B CP, you need to refer to the XML definition document which Openreach publish as part of the release documentation. If you are a portal CP, most of these character length validations will be carried out by the portal during your order or fault placement journey.
Raise and Manage a Customer Fault - Introduction
15

## Slide 16: Practice for the CP IT Design Community
End Customer and Home/Premises Environment Information
16
Field Name | Character Limit | Amendable | Description
//EndUserParty/Party/TroubleReportContact/DetailedContact/ContactName | 50 | Amendable | Provide the name of the person who is expected to be available at site when our engineer visits to resolve the problem with the service.
//EndUserParty/Party/TroubleReportContact/DetailedContact/Telephone | 11 | Amendable | The engineer will ring your customer on this number prior to arrival or if they are unable to locate or gain access to the premises.
//EndUserParty/Party/TroubleReportContact/DetailedContact/SecondaryTelephone | 11 | Amendable | The engineer may ring your customer on this number if required prior to arrival or if they are unable to locate or gain access to the premises.
//EndUserParty/Party/TroubleReportContact/DetailedContact/Email | 100 | Amendable | Provide the email ID of the contact person at the site. If you have opted in to use View My Engineer (VME) and have submitted preferences for Openreach to send email notifications direct to your end customers, Email notifications will make use of the DetailedContact/ElectronicMail field (the email address associated with the main contact). A valid email address must be provided for this service to work.
//AlternativeEndUserParty/Party/TroubleReportContact/DetailedContact/ContactName | 50 | Amendable | Also provide the name of a person who can be contacted alternatively if the primary contact person provided is not available.
//AlternativeEndUserParty/Party/TroubleReportContact/DetailedContact/Telephone | 11 | Amendable | In case the primary contact is not available, the engineer will ring your alternative contact on this number prior to arrival or if they are unable to locate or gain access to the premise

## Slide 17: Practice for the CP IT Design Community
End Customer and Home/Premises Environment Information
17
Field Name | Character Limit | Amendable | Description
//EndUserParty/Party/TroubleReportContactDetailedContact/CompanyName | 100 | Amendable | When placing a fault for a customer at business address, you should add the business name to the ‘CompanyName’ field within the fault. This should be “the name above the shop door” i.e. the information that should be visible to the engineer. For example although the customer contracting for the telephone service maybe “Dixons Stores Group”, it is better to supply the name for a given locations as “PC World Currys“
//TroubleReportDetail/AccessDetails/HSHazards | 100 | Amendable | Health & Safety related information should be supplied on all order types. If there are none, then the word ‘NONE’ should be written. E.g. Flat Roof, RAMS Statement Fragile Roof, Hot Site, Dog On-site, Dangerous Animals, Railway Working, Working at Height restrictions apply, High Voltage Overhead power lines in vicinity of work area, Asbestos Hazard
//TroubleReportDetail/AccessDetails/Notes | 255 | Amendable | Information about access to site for visit
//AccessDetails/EarliestNextAccessDateTime | 19 | Amendable | Earliest time end customer will be available at the property [DD/MM/YYYY HH:MM:SS]
//AccessDetails/LatestAccessDateTime | 19 | Amendable | Latest time end customer will be available at the property [DD/MM/YYYY HH:MM:SS]
//TroubleReportDetail/StandardQuestions/TwentyFourHourAccess | 1 | Not Amendable | Can the engineer attend the premises 24 hours a day. Y or N [1 Character]. Please note, 24 access is only available on Care Levels 4, 30 and 40.

## Slide 18: Practice for the CP IT Design Community
Service Related Information
18
Field Name | Character Limit | Amendable | Description
//TroubleReportDetail/ServiceId/Ident | 100 | Not Amendable | The service identifier as Openreach knows this
/TroubleReportDetail/VoiceServiceDN | 11 | Not Amendable | If a voice service has been provided over a non-WLR3 service, please provide the destination number of the service to enable testing and service restoration if required
//TroubleReportDetail/ServiceLevel | 4 | Not Amendable | The Service Maintenance Levels of the fault, this should be values 1, 2, 2.5, 3 & 4 to reflect the current service levels but will include values 20, 30 & 40 when Harmonised Repair is introduced
//TroubleReportDetail/OrderRevisedServiceLevel | 1 | Not Amendable | Indicates whether a CP wants to purchase Harmonised Repair. Date type: String Length: 1 LoV: Y,N
//TroubleReportDetail/ShortDescription | 80 | Amendable | A description of the issue experience by the end customer in their language
//TroubleReportDetail/ListOfNote/Note | 5000 | Amendable | Any information that is relevant to the engineering visit can be provided in this field. You can provided key information about the services provided to your customer in this field and any history or diagnostic information that will assist our engineer resolving your customer issue.
//TroubleReportDetail/FaultCode | 4 | Not Amendable | This is the code indicating the nature of the fault following your structured questioning and diagnostics with the end customer
//TroubleReportDetail/Appointment/Reference/RefNum | 8/9 | Amendable | Reference Number of Appointment obtained via the appointing dialogue services

## Slide 19: Practice for the CP IT Design Community
Service Related Information
19
Field Name | Character Limit | Amendable | Description
//TroubleReportDetail/TestReference/PerformerReference/InvocationIdentifier/RefNum | 64 | Not Amendable | This is the reference number of the line test that you have previously run via the line test dialogue service. This is mandatory if ‘No Test Reason’ is not provided
//TroubleReportDetail/StandardQuestions/DisruptiveTestsAllowed | 1 | Not Amendable | This indicates that you are willing for services to be disrupted that maybe required to resolve the issue reported. Values Y or N
//TroubleReportDetail/NoTestReason | 80 | Not Amendable | This is required if a line test was not successfully completed or not applicable
//TroubleReportDetail/TestProduct | 15 | Not Amendable | Request for additional testing the CP requires the engineer to perform
//TroubleReportDetail/TestAccountDetails | 255 | Amendable | This is for the CP to provide the test account, user name, password, IP and URL
//TroubleReportDetail/AcceptAdditionalCharges | 1 | Not Amendable | When you expedite a fault you need to pre-authorise additional charges. Y or N
//TroubleReportDetail/UpperTRCBand | 1 | Amendable | This indicates the upper level of banding pre-authorised to enable engineer may need to complete. Values 0,1,2, 3, & 4
//TroubleReportDetail/AcceptTermsAndConditionsCharges | 1 | Not Amendable | When you expedite a fault you need to accept the terms and conditions this also applies in you are selecting a chargeable appointment. Y or N

## Slide 20: Practice for the CP IT Design Community
CP Related Information
20
Field Name | Character Limit | Amendable | Description
//CooperationArrangements/Co-OpCallRequested | 1 | Amendable | In some circumstances an engineer will need to co-op with the CPs technical department to isolate the issues or restore service, please indicate if you are able to support inbound co-op calls
//CooperationArrangements/Co-OpLocation | 100 | Amendable | For some product variants a CP can request for a joint meet at either the exchange or the customer location
/CooperationArrangements/Co-OpDateTime | 19 | Amendable | For some product variants a CP can request a specific data and time for the joint meet [DD/MM/YYYY HH:MM:SS]
//CooperationArrangements/TroubleReportParty/Co-OpParty/Party/TroubleReportContact/DetailedContact/ContactName | 50 | Amendable | Name of technical department or CP engineer who will be attending the joint meeting
//CooperationArrangements/TroubleReportParty/Co-OpParty/Party/TroubleReportContact/DetailedContact/Telephone | 11 | Amendable | Number of technical department or CP engineer who will be attending the joint meeting
//CooperationArrangements/ListOfNote/Note | 5000 | Amendable | Co-Op and/or join meet contact notes

## Slide 21: Practice for the CP IT Design Community
CP Related Information
21
Field Name | Character Limit | Amendable | Description
//TroubleReportReference/ReportingReference/Reference/RefNum | 64 | Amendable | The reference number as the CP would know this for the fault
//TroubleReportHeader/TroubleReportParty/ReportingParty/Party@PartyID | 13 | Amendable | This is code entered by the CP organisation that represents the party trading with Openreach
//TroubleReportContact/DetailedContact/ContactName | 50 | Amendable | Last Name of the person within your organisation to contact for any enquiries
//TroubleReportContact/DetailedContact/FirstName | 50 | Amendable | First Name of the person within your organisation to contact for any enquiries
//TroubleReportContact/DetailedContact/Telephone | 11 | Amendable | Number to call within your organisation to contact for any enquiries
//TroubleReportContact/DetailedContact/Email | 100 | Amendable | E-mail address to mail to within your organisation to contact for any enquiries

## Slide 22: Appendix A
RAMS statements
RAMS Statement for inclusion within HSHazard Notes
RAMS Generic supplied to customer
RAMS 1 Cabling at EU Premises supplied to customer
RAMS 3 Blown Fibre at EU Premises supplied to customer
RAMS 4 Pole Erection / Cabling supplied to customer
RAMS 6 Installation of Wideband Eqpt supplied to customer
RAMS 7 Installation of Ductwork supplied to customer
RAMS 8 Working at Airports supplied to customer
RAMS 9 Surveying for cabling at Airports supplied to customer
RAMS 10 Working in the Overhead Network supplied to customer
RAMS 11 Cabling and Working in UG Structures supplied to customer
RAMS 12 Internal Cabling / NTEs supplied to customer
RAMS 16 Surveying an Office Building supplied to customer
RAMS 20 Provision of PSTN supplied to customer
22

## Slide 23: Appendix B
If you have been advised via Manage Line Plant Availability (MLPA) or the Line Test Dialogue Service that the premises is served by an internal Distribution Point, this will indicate that one is located somewhere inside your customer’s building or building complex and could be in a room that requires separate access, an example of what an Internal DP looks like is illustrated below
Example Internal DP
23

## Slide 24: Appendix C
Long Description Example Questions – Part 1 Data Source Legend - EC = End Customer, CP = Communication Provider
No. | Question Description | Sample Answers | Data Source
1 | When did the Problem First Occur? | i.e. 01/12/2015 | EC
1A | When did the service last work? | i.e. 01/12/2015 | EC
2 | Has your service ever worked? | Yes/No | EC or CP
3 | Have you made any recent changes to your service? | Yes/No - if yes please indicate i.e. Broadband speed capped (CP provided) OR New router installed (EC or CP) OR a New Line has been provided OR Transfer of service recently completed (EC provided) | EC or CP
4 | What equipment/service is the End Customer using on this line that is impacted by this Problem? | e.g. Phone, STB, HD TV, Cisco Ethernet Router etc. | EC
5 | Where is the impacted service located? | e.g. office 7 floor 2, STB in living room, router in study, etc | EC
6 | What services are impacted by this Problem e.g. Broadband or Voice? | broadband and voice, BB, TV and Voice, BB only, Bonded Copper Solution etc. | EC or CP
7 | Is the End Customer able to receive incoming calls and make outgoing calls? | Incoming and Outgoing, Incoming Only, Outgoing Only, None or Not Using Voice Service. (Record if the voice service is also faulty or if the customer is unable to verify if the voice service is working) | EC
8 | Is the End customer experiencing problems on all calls or only certain numbers? | All calls or certain numbers only | EC
9 | What numbers does the End Customer experience problems to/from? | e.g. All numbers or 0800800151 and 01234567890 | EC
10 | Is the Problem intermittent or permanent? | Intermittant or Permanent | EC or CP
11 | Is the Problem a total loss or partial loss of service? | Total Loss or Partial Loss | EC or CP
12 | Frequency & Duraton of Problem ? | Only if intermittant - e.g. every day for 2hrs | EC or CP
13 | Is there a regular pattern to the problem and if so what is it and when? | e.g. Every day between 20:00 and 22:00 | EC or CP
14 | Do your own test results indicate a fault condition? | Yes or No | CP
15 | What is the fault condition your test results indicate? | ???? | CP
16 | Is there any action that does temporarily fix the problem? | Yes - reboots router | EC or CP
24

## Slide 25: Appendix C
Long Description Example Questions – Part 2 Data Source Legend - EC = End Customer, CP = Communication Provider
No. | Question Description | Sample Answers | Data Source
17 | Is the broadband service fixed or rate adaptive? | Fixed/Adaptive | CP
18 | Is there any rate capping on the Broadband service? | Yes capped at 40down/10up | CP
19 | Is the Broadband speed stable? | Yes/No | EC or CP
19A | Has the broadband speed deteriorated | Yes/No | EC or CP
20 | What is the expected Broadband Downstream Sync Speed? | Value | EC or CP
21 | What is the current Broadband Downstream Sync Speed? | Value | EC or CP
22 | What is the expected Broadband Upstream Sync Speed? | Value | EC or CP
23 | What is the current Broadband Upstream Sync Speed? | Value | EC or CP
24 | What is the Broadband Interleaving status? | i.e. Fast | CP
25 | What is the Down Stream Loop Loss? | Value | CP
26 | What is the Down Stream Loop Loss Max? | Value | CP
27 | What is the Down Stream Margin? | Value | CP
28 | What is the Down Stream Margin Max-Min? | Value | CP
29 | What is the Down Stream Errored Seconds? | Value | CP
30 | What is the Down Stream HEC Errors? | Value | CP
31 | What is the Up Stream Loop Loss? | Value | CP
32 | What is the Up Stream Loop Loss Max-Min? | Value | CP
33 | What is the Up Stream Margin? | Value | CP
34 | What is the Up Stream Margin Max-Min? | Value | CP
35 | What is the Up Stream Errored Seconds? | Value | CP
36 | What is the Up Stream HEC Errors? | Value | CP
25

## Slide 26: Appendix D
Fault Codes explained - Part 1
Fault Code | Fault Description | Applicable to WLR3 | Applicable to LLU | Applicable to FTTC
BNR | Bell not Ringing | Yes | Yes (Post V30) | Yes (Post V30)
BR | Bell Ringing Continuous | Yes | Yes (Post V30) | Yes (Post V30)
CCS | Customer Control Services (Call Minder) | Yes | No | No
CDT | Continuous Dial Tone | Yes | Yes (Post V30) | Yes (Post V30)
CO | Cutting Off | Yes | Yes (Post V30) | Yes (Post V30)
DRM | Damage Report Modem | Yes (Post V30) | Yes (Post V30) | Yes
DRN | Damage Report NTE | Yes (Post V30) | Yes (Post V30) | Yes
DRO | Damage Report Overhead | Yes | Yes (Post V30) | Yes
DRU | Damage Report Underground | Yes | Yes (Post V30) | Yes
DRW | Damage Report Wiring | Yes | Yes (Post V30) | Yes
DRA | Damage Report Apparatus | Yes | Yes (Post V30) | Yes (Post V30)
FNT | Faint Transmission | Yes | Yes (Post V30) | Yes (Post V30)
MOD | Modulation/Modem/Modify (Up for debate) | Yes | No | No
NDT | No Dial Tone | Yes | Yes (Post V30) | Yes (Post V30)
NR | No Reply | Yes | Yes (Post V30) | Yes (Post V30)
NSY | Noisy | Yes | Yes (Post V30) | Yes (Post V30)
NT | No Tones | Yes | Yes (Post V30) | Yes (Post V30)
NU | Number Unobtainable | Yes | Yes (Post V30) | Yes (Post V30)
OHR | Overhearing | Yes | Yes (Post V30) | Yes (Post V30)
OWT | One Way Transmission | Yes | Yes (Post V30) | Yes (Post V30)
PET | Permanent Engaged Tone | Yes | Yes (Post V30) | Yes (Post V30)
RTP | Ring Trip | Yes | Yes (Post V30) | Yes (Post V30)
26

## Slide 27: Appendix D
Fault Codes explained - Part 2
Fault Code | Fault Description | Applicable to WLR3 | Applicable to LLU | Applicable to FTTC
UTR | Unable to Ring Trip | Yes | Yes (Post V30) | Yes (Post V30)
WNO | Wrong Number Outgoing | Yes | Yes (Post V30) | Yes (Post V30)
XL | Crossed Lines | Yes | Yes (Post V30) | Yes (Post V30)
ESF | Exchange Service Facility | Yes | No | No
CIA | Connection Intermittent & Modem Power Light Off | Yes (Post V30) | Yes (Post V30) | Yes
CIB | Connection Intermittent & Modem Power Light On & Modem Sync Steady Green | Yes (Post V30) | Yes (Post V30) | Yes
CIC | Connection Intermittent & Modem Power Light On & Modem Sync Flashing | Yes (Post V30) | Yes (Post V30) | Yes
CID | Connection Intermittent & Modem Power Light On & Modem Sync Light Off | Yes (Post V30) | Yes (Post V30) | Yes
CPA | Connection Permanent & Modem Power Light Off | Yes (Post V30) | Yes (Post V30) | Yes
CPB | Connection Permanent & Modem Power Light On & Modem Sync Steady Green | Yes (Post V30) | Yes (Post V30) | Yes
CPC | Connection Permanent & Modem Power Light On & Modem Sync Flashing | Yes (Post V30) | Yes (Post V30) | Yes
CPD | Connection Permanent & Modem Power Light On & Modem Sync Off | Yes (Post V30) | Yes (Post V30) | Yes
PIA | Performance Intermittent & Modem Power Light Off | Yes (Post V30) | Yes (Post V30) | Yes
PIB | Performance Intermittent & Modem Power Light On & Modem Sync Steady Green | Yes (Post V30) | Yes (Post V30) | Yes
PIC | Performance Intermittent & Modem Power Light On & Modem Sync Flashing | Yes (Post V30) | Yes (Post V30) | Yes
PID | Performance Intermittent & Modem Power Light On & Modem Sync Off | Yes (Post V30) | Yes (Post V30) | Yes
PPA | Performance Permanent & Modem Power Light Off | Yes (Post V30) | Yes (Post V30) | Yes
PPB | Performance Permanent & Modem Power Light On & Modem Sync Steady Green | Yes (Post V30) | Yes (Post V30) | Yes
PPC | Performance Permanent & Modem Power Light On & Modem Sync Flashing | Yes (Post V30) | Yes (Post V30) | Yes
PPD | Performance Permanent & Modem Power Light On & Modem Sync Off | Yes (Post V30) | Yes (Post V30) | Yes
WIF | WIFI Intermittent | Yes (Post V30) | Yes (Post V30) | Yes (Post V30)
27

## Slide 28: Appendix E
Major Cable Breakdown
The UK Cable Breakdown Summary, which provides details of cable breakdowns in the copper exchange-side network. Updated every 2hours, 24 hours a day, every day of the year. To request access please send an email to uk.cable.breakdown.g@bt.com and complete the subject field with Access to UK Cable Breakdown Summary, clearly stating your name, e-mail address and the Communications Provider you work for.
Major Service Outage
This process will provide you with information on Major Service Outage (MSO)in the Access Network. The tool monitors the access network using broadband data to identify cable breaks resulting from either theft or third party damage. For these incidents Openreach is able to proactively advise CPs by sending emails containing the postcodes of the affected end users. If you are interested register by emailing cablealert@openreach.co.uk confirming the email address(s) you wish notifications to be sent to.
Online materials on how the tool works and some frequently asked questions available via the Openreach Portal: www.openreach.co.uk/orpg/home/helpandsupport/how-toguides/howtoguides.do
Major Cable Breakdown/Service Outage
28

## Slide 29: Appendix F
View My Engineer (VME) was launched to Industry on 7 September 2015 across WLR (with the exception of ISDN30), LLU, NGA and SBS (except Business Connections).
View My Engineer (VME) is a real time, proactive update service to give CP’s and end customers information on the progress of the engineering element of their provision or repair.
VME is available to all CP’s on the Order and Fault Tracker self-service tool –Quick Search View.
6 different potential milestones as the job progresses through the journey.
If you register for VME preferences, you can take advantage of proactive notifications.
Charging
B2B gateway sent to the CP (XML/KCI): No charge
Email sent directly from Openreach to end customers: No charge
SMS sent directly from Openreach to end customers: Openreach will charge per SMS sent in accordance with the VME commercial terms
The charges will be invoiced quarterly
View My Engineer (VME) FAQ’s:
https://www.openreach.co.uk/orpg/home/helpandsupport/how-toguides/howtoguides.do
View My Engineer
29